## Slide 1
자동 차고문
2021042037 김건우

## Slide 2: 목차
과제 개요
과제 필요성
개발 목표
프로젝트 설계
개발 일정
중간 결과2

## Slide 3: 과제 개요
차량 번호판을 인식하여
다른 차량이 들어가지 못하는 차고

## Slide 4: 과제 필요성
편의성
  문이 자동으로 열리기 때문에 편리하다.
보안성
  다른 차량이 들어오지 못해 보안이 좋다.

## Slide 5: 개발 목표
차량이 들어오는 것을 초음파 센서로 인식
번호판 인식
차고 주인의 차량과 차량 번호가 같으면 문이 열림

## Slide 6
초음파 센서(문)
컴퓨터
물체(차)
인식
사진 촬영
웹캠
사진 전송
컴퓨터
번호판 인식
스텝모터
(문 열기)
번호판이 없거나 번호가 다름
초음파 센서(문)초음파 센서(차고)
물체(차)
인식
스텝모터
(문 닫기)
초음파 센서(차고)
물체(차)
인식
스텝모터
(문 열기)
초음파 센서(차고)
초음파 센서(문)
물체(차)
인식
스텝모터
(문 닫기)
SW 구조

## Slide 7
H/W 구조
카메라
(바닥에서 5cm 위)
초음파 센서(차고)
(바닥에서 5cm 위)
스텝모터
아두이노
컴퓨터
초음파 센서(문)
(바닥에서 5cm 위)
차체
가로: 약 22cm
세로: 약 35cm
높이: 약 19cm
30cm
40cm
25cm

## Slide 8: 개발 일정
Month | Week | 목표 | 실적
10월 | 1~2주 | 차량 인식 | 완료
 | 3~4주 | 차량 번호판 인식 | 완료
11월 | 1~2주 | 차량 번호판 인식 | 
 | 3~4주 | 차고 문 제어 | 완료
12월 | 1~2주 | 오류 개선 및 하드웨어 제작 | 

## Slide 9: 중간 결과
진행 과정
  모든 기능 제작 완료
문제점
  번호판 인식이 생각보다 정확하지 않음
  가끔씩 알 수 없는 이유로 프로그램이 종료됨

## Slide 10
if car_in == False: #arduino while (True): grabbed, frame = video_capture.read() #사진 촬영 cv2.imshow('Original Video', frame) if ser.readable(): val_door = ser.readline() #아두이노 시리얼 보드 읽어오기 print(val_door.decode()[:len(val_door)-1]) # 넘어온 데이터 중 마지막 개행문자 제외 print('cm') # camera capture if int(val_door.decode()[:len(val_door)-1]) <= 10: #초음파 센서와의 거리가 10cm 이하일 때 file = datetime.datetime.now().strftime("%Y%m%d_%H%M%S%f") + '.jpg' #사진 저장 cv2.imwrite(file, frame) print(file, ' saved') break
직접 짠 코드 (python)

## Slide 11
#2 img_ori = cv2.imread(file) #img_ori = cv2.imread("car2.png") height, width, channel = img_ori.shape #plt.figure(figsize=(12, 10)) #plt.imshow(img_ori,cmap='gray') #print(height, width, channel) #3 gray = cv2.cvtColor(img_ori, cv2.COLOR_BGR2GRAY) #plt.figure(figsize=(12,10)) #plt.imshow(gray, cmap='gray') #plt.show() #4 img_blurred = cv2.GaussianBlur(gray, ksize=(5, 5), sigmaX=0) img_blur_thresh = cv2.adaptiveThreshold( img_blurred, maxValue=255.0, adaptiveMethod=cv2.ADAPTIVE_THRESH_GAUSSIAN_C, thresholdType=cv2.THRESH_BINARY_INV, blockSize=19, C=9 ) #4-1 img_thresh = cv2.adaptiveThreshold( gray, maxValue=255.0, adaptiveMethod=cv2.ADAPTIVE_THRESH_GAUSSIAN_C, thresholdType=cv2.THRESH_BINARY_INV, blockSize=19, C=9 ) #plt.figure(figsize=(20,20)) #plt.subplot(1,2,1) #plt.title('Threshold only') #plt.imshow(img_thresh, cmap='gray') #plt.subplot(1,2,2) #plt.title('Blur and Threshold') #plt.imshow(img_blur_thresh, cmap='gray')
오픈소스
(python)

## Slide 12
#5 contours, _ = cv2.findContours( img_blur_thresh, mode=cv2.RETR_LIST, method=cv2.CHAIN_APPROX_SIMPLE ) temp_result = np.zeros((height, width, channel), dtype=np.uint8) cv2.drawContours(temp_result, contours=contours, contourIdx=-1, color=(255,255,255)) #plt.figure(figsize=(12, 10)) #plt.imshow(temp_result) #6 temp_result = np.zeros((height, width, channel), dtype=np.uint8) contours_dict = [] for contour in contours: x, y, w, h = cv2.boundingRect(contour) cv2.rectangle(temp_result, pt1=(x, y), pt2=(x + w, y + h), color=(255, 255, 255), thickness=2) contours_dict.append({ 'contour': contour, 'x': x, 'y': y, 'w': w, 'h': h, 'cx': x + (w / 2), 'cy': y + (h / 2) }) #plt.figure(figsize=(12, 10)) #plt.imshow(temp_result, cmap='gray')
오픈소스
(python)

## Slide 13
#7 MIN_AREA = 80 MIN_WIDTH, MIN_HEIGHT = 2, 8 MIN_RATIO, MAX_RATIO = 0.25, 1.0 possible_contours = [] cnt = 0 for d in contours_dict: area = d['w'] * d['h'] ratio = d['w'] / d['h'] if area > MIN_AREA \ and d['w'] > MIN_WIDTH and d['h'] > MIN_HEIGHT \ and MIN_RATIO < ratio < MAX_RATIO: d['idx'] = cnt cnt += 1 possible_contours.append(d) temp_result = np.zeros((height, width, channel), dtype=np.uint8) for d in possible_contours: cv2.rectangle(temp_result, pt1=(d['x'], d['y']), pt2=(d['x'] + d['w'], d['y'] + d['h']), color=(255, 255, 255), thickness=2) #plt.figure(figsize=(12, 10)) #plt.imshow(temp_result, cmap='gray') #8 MAX_DIAG_MULTIPLYER = 5 MAX_ANGLE_DIFF = 12.0 MAX_AREA_DIFF = 0.5 MAX_WIDTH_DIFF = 0.8 MAX_HEIGHT_DIFF = 0.2 MIN_N_MATCHED = 3
오픈소스
(python)

## Slide 14
def find_chars(contour_list): matched_result_idx = [] for d1 in contour_list: matched_contours_idx = [] for d2 in contour_list: if d1['idx'] == d2['idx']: continue dx = abs(d1['cx'] - d2['cx']) dy = abs(d1['cy'] - d2['cy']) diagonal_length1 = np.sqrt(d1['w'] ** 2 + d1['h'] ** 2) distance = np.linalg.norm(np.array([d1['cx'], d1['cy']]) - np.array([d2['cx'], d2['cy']])) if dx == 0: angle_diff = 90 else: angle_diff = np.degrees(np.arctan(dy / dx)) area_diff = abs(d1['w'] * d1['h'] - d2['w'] * d2['h']) / (d1['w'] * d1['h']) width_diff = abs(d1['w'] - d2['w']) / d1['w'] height_diff = abs(d1['h'] - d2['h']) / d1['h'] if distance < diagonal_length1 * MAX_DIAG_MULTIPLYER \ and angle_diff < MAX_ANGLE_DIFF and area_diff < MAX_AREA_DIFF \ and width_diff < MAX_WIDTH_DIFF and height_diff < MAX_HEIGHT_DIFF: matched_contours_idx.append(d2['idx']) matched_contours_idx.append(d1['idx']) if len(matched_contours_idx) < MIN_N_MATCHED: continue matched_result_idx.append(matched_contours_idx) unmatched_contour_idx = [] for d4 in contour_list: if d4['idx'] not in matched_contours_idx: unmatched_contour_idx.append(d4['idx']) unmatched_contour = np.take(possible_contours, unmatched_contour_idx) recursive_contour_list = find_chars(unmatched_contour) for idx in recursive_contour_list: matched_result_idx.append(idx) break return matched_result_idx result_idx = find_chars(possible_contours) matched_result = [] for idx_list in result_idx: matched_result.append(np.take(possible_contours, idx_list)) temp_result = np.zeros((height, width, channel), dtype=np.uint8) for r in matched_result: for d in r: cv2.rectangle(temp_result, pt1=(d['x'], d['y']), pt2=(d['x'] + d['w'], d['y'] + d['h']), color=(255, 255, 255), thickness=2) #plt.figure(figsize=(12, 10)) #plt.imshow(temp_result, cmap='gray')
오픈소스
(python)

## Slide 15
#9 PLATE_WIDTH_PADDING = 1.3 # 1.3 PLATE_HEIGHT_PADDING = 1.5 # 1.5 MIN_PLATE_RATIO = 3 MAX_PLATE_RATIO = 10 plate_imgs = [] plate_infos = [] for i, matched_chars in enumerate(matched_result): sorted_chars = sorted(matched_chars, key=lambda x: x['cx']) plate_cx = (sorted_chars[0]['cx'] + sorted_chars[-1]['cx']) / 2 plate_cy = (sorted_chars[0]['cy'] + sorted_chars[-1]['cy']) / 2 plate_width = (sorted_chars[-1]['x'] + sorted_chars[-1]['w'] - sorted_chars[0]['x']) * PLATE_WIDTH_PADDING sum_height = 0 for d in sorted_chars: sum_height += d['h'] plate_height = int(sum_height / len(sorted_chars) * PLATE_HEIGHT_PADDING) triangle_height = sorted_chars[-1]['cy'] - sorted_chars[0]['cy'] triangle_hypotenus = np.linalg.norm( np.array([sorted_chars[0]['cx'], sorted_chars[0]['cy']]) - np.array([sorted_chars[-1]['cx'], sorted_chars[-1]['cy']]) ) angle = np.degrees(np.arcsin(triangle_height / triangle_hypotenus)) rotation_matrix = cv2.getRotationMatrix2D(center=(plate_cx, plate_cy), angle=angle, scale=1.0) img_rotated = cv2.warpAffine(img_thresh, M=rotation_matrix, dsize=(width, height)) img_cropped = cv2.getRectSubPix( img_rotated, patchSize=(int(plate_width), int(plate_height)), center=(int(plate_cx), int(plate_cy)) ) if img_cropped.shape[1] / img_cropped.shape[0] < MIN_PLATE_RATIO or img_cropped.shape[1] / img_cropped.shape[ 0] < MIN_PLATE_RATIO > MAX_PLATE_RATIO: continue plate_imgs.append(img_cropped) plate_infos.append({ 'x': int(plate_cx - plate_width / 2), 'y': int(plate_cy - plate_height / 2), 'w': int(plate_width), 'h': int(plate_height) }) #plt.subplot(len(matched_result), 1, i + 1) #plt.imshow(img_cropped, cmap='gray')
오픈소스
(python)

## Slide 16
#11 longest_idx, longest_text = -1, 0 plate_chars = [] for i, plate_img in enumerate(plate_imgs): plate_img = cv2.resize(plate_img, dsize=(0, 0), fx=1.6, fy=1.6) _, plate_img = cv2.threshold(plate_img, thresh=0.0, maxval=255.0, type=cv2.THRESH_BINARY | cv2.THRESH_OTSU) # find contours again (same as above) contours, _ = cv2.findContours(plate_img, mode=cv2.RETR_LIST, method=cv2.CHAIN_APPROX_SIMPLE) plate_min_x, plate_min_y = plate_img.shape[1], plate_img.shape[0] plate_max_x, plate_max_y = 0, 0 for contour in contours: x, y, w, h = cv2.boundingRect(contour) area = w * h ratio = w / h if area > MIN_AREA \ and w > MIN_WIDTH and h > MIN_HEIGHT \ and MIN_RATIO < ratio < MAX_RATIO: if x < plate_min_x: plate_min_x = x if y < plate_min_y: plate_min_y = y if x + w > plate_max_x: plate_max_x = x + w if y + h > plate_max_y: plate_max_y = y + h img_result = plate_img[plate_min_y:plate_max_y, plate_min_x:plate_max_x] img_result = cv2.GaussianBlur(img_result, ksize=(3, 3), sigmaX=0) _, img_result = cv2.threshold(img_result, thresh=0.0, maxval=255.0, type=cv2.THRESH_BINARY | cv2.THRESH_OTSU) img_result = cv2.copyMakeBorder(img_result, top=10, bottom=10, left=10, right=10, borderType=cv2.BORDER_CONSTANT, value=(0, 0, 0)) pytesseract.pytesseract.tesseract_cmd = 'C:/tesseract/tesseract.exe' chars = pytesseract.image_to_string(img_result, lang='kor', config='--psm 7 --oem 0') result_chars = '' has_digit = False for c in chars: if ord('가') <= ord(c) <= ord('힣') or c.isdigit(): if c.isdigit(): has_digit = True result_chars += c #print(result_chars) plate_chars.append(result_chars) if has_digit and len(result_chars) > longest_text: longest_idx = i #12 #plt.subplot(len(plate_imgs), 1, i + 1) #plt.imshow(img_result, cmap='gray')
오픈소스
(python)

## Slide 17
if longest_idx >= 0: info = plate_infos[longest_idx] chars = plate_chars[longest_idx] print(chars) if host_car_number1 in chars or host_car_number2 in chars or host_car_number3 in chars or host_car_number4 in chars: count = count + 1 print(count, "카운트") else: remove(file) print(file, "removed") if count >= 2: commend = 'a' ser.write(commend.encode()) commend = 'b' ser.write(commend.encode()) count = 0 car_in = True; else: remove(file) print(file, "removed") else: if ser.readable(): val_garage = ser.readline() print(val_garage.decode()[:len(val_garage) - 1]) # 넘어온 데이터 중 마지막 개행문자 제외 # camera capture if int(val_garage.decode()[:len(val_garage) - 1]) == 10000: car_in = False
직접 짠 코드
(python)

## Slide 18
long duration_door, distance_door, duration_garage, distance_garage;
delayMicroseconds(2); //문 초음파 센서 거리 감지
digitalWrite(TRIG_DOOR, HIGH);
delayMicroseconds(10);
digitalWrite(TRIG_DOOR, LOW);
duration_door = pulseIn(ECHO_DOOR, HIGH);
delayMicroseconds(2); //차고 초음파 센서 거리 감지
digitalWrite(TRIG_GARAGE, HIGH);
delayMicroseconds(10);
digitalWrite(TRIG_GARAGE, LOW);
duration_garage = pulseIn(ECHO_GARAGE, HIGH);
distance_door = duration_door * 17 / 1000;
distance_garage = duration_garage * 17 / 1000;
직접 짠 코드
(arduino)

## Slide 19
if(car_in == false){ //차가 차고에 없다면
Serial.println(distance_door); //문 초음파 센서 거리 출력
delay(50);
if(Serial.available()){
cmd = Serial.read();
}
if(cmd == 'a’){ //a가 읽히면
if(!door_open){ //차고의 문을 연다
myStepper.step(stepsPerRevolution);
car_in = true;
door_open = true;
in = true;
}
}
}
else{ //차가 차고에 있다면
if(door_open){ //문이 열려있다면
if(distance_garage <= 10 && distance_door > 10){ //차가 문에서 감지되지 않고 차고에서 감지됐을 때
if(in == true){ //차가 들어올 때
myStepper.step(-stepsPerRevolution); //문을 닫는다
door_open = false;
in = false;
}
}
직접 짠 코드
(arduino)

## Slide 20
else if(distance_garage > 10 && distance_door <= 10){ //차가 차고에서 감지되지 않고 문에서 감지됐을 때
if(in == false){ //차가 나갈 때
myStepper.step(-stepsPerRevolution);
door_open = false;
Serial.println(10000); //10000을 출력한다
car_in = false;
}
}
}
else{ //문이 닫혀있을 때
if(distance_garage > 10){ //차가 차고에서 감지되지 않으면
myStepper.step(stepsPerRevolution); //문을 연다
door_open = true;
}
}
}
delay(500);
직접 짠 코드
(arduino)